## Slide 1: Oregon State University NASA USLI
12/14/2017

## Slide 3: Structural Overview
45.2 lbs. at launch
5.4” diameter
116” (9.7 ft.) length
Estimated Altitude: 5,900 ft.

## Slide 4: Body Materials
Carbon Fiber Airframe
  2 sections, 50” (4.2 ft.) and 46” (3.8 ft.)
Fiberglass Coupler Tubes
  2 coupler sections, 8” each

## Slide 5: Nosecone and Bulkheads
Nosecone:
Fiberglass with aluminum tip
5 Bulkheads, 2 Centering Rings
  Carbon fiber and Nomex
  0.38” Nomex
  0.024” carbon fiber

## Slide 6: Recovery Overview: Aft Section

## Slide 7: Recovery Overview: Fore Section

## Slide 8: Aerodynamics/Recovery: Ejection
Black Powder Ejection Charges
Separation: Missile Works RRC3
Parachute Release: Jolly Logic Chute Release

## Slide 9: Aerodynamics/Recovery: Parachutes
Drogue Velocities: ~130 ft/s
Main Velocities: ~13 ft/s

## Slide 10: Rover Payload: Overview
Technical Specifications
5.05 pounds
4.9 inches in diameter
3 ft/s top speed
10.625 inches long

## Slide 11: Rover Payload: Drive Train
7.81 lbs.-in. max torque
Carbon fiber axle
¾” thick HDPE wheel
Load dissipation from wheel through U-block

## Slide 13: Rover Payload: Chassis
0.25” carbon-fiber rods
Aluminum joints
Drivetrain and electronics attached inside
High compressive strength

## Slide 14: Rover Payload: Solar Deployment

## Slide 15: Rover Payload: Solar Deployment

## Slide 18: Rover Payload: Ejection
Black powder ejection upon landing

## Slide 19: Rover Payload: Ejection Testing

## Slide 20: Rover Payload: Electronics

## Slide 21: Questions?

## Slide 22: Match Rockets
Newton’s Third Law of Motion
    Action – Combustion
    Re-Action – products (hot gas and smoke) create movement
Newton’s Second
Law of Motion
Force (thrust) is the product of
mass escaping and its acceleration

## Slide 23: Match Rockets
Instructions
Cut two square of Aluminum foil (one body length, second much smaller)
Roll the large square over a thin circular body until it’s a tube
Gently pinch down one side and wrap the smaller square around it. (this will be your nosecone)
Fins are optional, but recommended. Cut a square piece of tape, poke a hole in the center and slide the rocket through the hole. Pinch the tape to create the fins. Cut off excess.

## Slide 24: Match Rockets
Instructions
Cut the tips off the matches. Only one to two match heads per rocket. Gently load and push toward the top.
Slide rocket onto paperclip stand and pinch down the exhaust port around the clip but still able to slide.
Stand back and allow one of the staff to light your rocket.

## Slide 25: Aerodynamics
Rocket aerodynamics is the study of how air flows over a rocket and how this affects drag and stability.
Nose cone and Fins => Designed to:
Minimize drag
Provide stability
Provide control

## Slide 26: Aerodynamics
  Stability in a rocket depends on the center of pressure
  being lower than the center of mass or the rocket
  will tumble.
increased distance = increased stability
Fins at the bottom of the rocket moves the center
of pressure down, but adds drag.
Finding the balance is the key.

## Slide 27: Paper Cone Flights
Instructions
Take you paper cone, add some playdough as a balancing weight inside the cone.
Create paper fins and try and achieve a stable decent

## Slide 28: Electro-magnetic Train
Wire Cutters
Copper Wire Coil
AAA Battery
Neodymium Magnets (Caution very strong)

## Slide 29: Electro-magnetic Train
Instructions
Take the two Neodymium magnets and flip them so that they repel each other and place the AAA battery between.
Insert into the copper coil and give slight push and watch your train leave.

## Slide 30: Electro-magnetic Train

## Slide 31: Electric Motor

## Slide 32: Electric Motor